## Slide 1
modelling timing Micromegas
(slightly refurbished compared to 1.5years ago)
D. Gonzalez-Diaz, F. Resnati, R. Veenhof,
CERN, 21/02/2017
T. Papaevangelou et al., arXiv:1601.00123v2

## Slide 2
idea: develop a simple code for taking technological decisions
Obtain MC solutions from a 1D hydrodynamic formalism under ‘reasonable’ assumptions:
Diffusion and drift parameters taken from Magboltz.
Assume statistical equilibrium in between ionizing collisions (Legler model).
Assume uniform fields in both drift and Micromegas regions; characterize electron transmission between them by a single parameter (T), modelled as a simple binomial process.
Add exponential fluctuations during Micromegas amplification (GMM).
Multiplication along the drift region (GD) and transmission (T) estimated from comparison between data and COMSOL simulations.
Calculate the induced signal from Ramo theorem, include capacitance and FEE.
Produce waveforms and apply a pulse-shape analysis similar to what is done in data.
Magboltz (hydro input) + COMSOL (hydro average solution) + MATLAB (hydro stochastic solution)

## Slide 3
OR
n: 3D electron density
z: direction of the electric field
units: [length0.5]
full 3D stochastic solution: computationally expensive
(use Garfield++ or, even better: Garfield++/microscopic)->R. Veenhof/S.Biagi
general hydrodynamic equations (field along z)
average solution
(e.g. COMSOL)
stochastic solution from
1D-MC (‘a la Legler’)
axi-symmetric model of microbulk micromegas (color code: electron density at a given time)
(single-electron induced signal)
bulk-MM
microbulk-MM

## Slide 4
input parameters for simulations: Ne–C2H6 (Magboltz)
5% C2H6
10% C2H6
15% C2H6
20% C2H6
100% C2H6
vd [μm/ps]
DL*/vd [ps/√μm]
α-η [μm-1]
DT* [μm /√μm]
R. Veenhof

## Slide 5
F. Resnati
100μm
average solutions from hydro (benchmark)
(Xe-TMA published data
with Garfield++/microscopic)
Modelling the behaviour of microbulk Micromegas in Xenon/trimethylamine gas
E. Ruiz-Choliz et al., NIM A, 799 (2015) 137-146.

## Slide 6
average solutions from hydro

## Slide 7
average solutions from hydro (transmission T and gain GD)
F. Resnati
30μm
100μm
gap: 50 μm
optical
transmission (T)
(simulation turning off pre-amplification)
EMM=90kV/cm
transmission x pre-amplification (TxGD)
effective gain G*≈2x105 (simulation)
0.07
160
2x104
G*(Edrift)≈ T x GD x GMM
Micromegas gain at full transmission
(GMM = G(T=1))

## Slide 8
note 1 (what about extraction efficiency?)
G* = T(Edrift, Eamp) x GD(Edrift) x GMM(EMM) x εext(Edrift )
Extraction efficiency probably just some 20%
shy of saturation at most.
Measurements of photoelectron extraction efficiency from CsI mixtures of Ne with CH4, CF4, CO2, N2
J. Escada et al., JINST, 4(2009)P11025

## Slide 9
note 2 (what about bulk MMs?)
G*(Edrift=10kV/cm) ≈ T x GD x GMM
0.07
160
20000
(no simulations yet)
G*(Edrift=10kV/cm) ≈ T x GD x GMM
0.8 (Topt)
160
assume these values in the following (if nothing else is said: Edrift = 10kV/cm)
~104
EMM=90kV/cm
EMM=40kV/cm
microbulk-MM (50um)
bulk-MM (128um)

## Slide 10
stochastic solutions from 1D-hydro

## Slide 11
important MC technical information
The MC arrival times of the electrons at the MM (after a random walk in the drift) can be computed analytically. Note: even in absence of multiplication it is not a Gaussian, although its rms approaches DL*/vd √gap! (hereafter: ‘spread from diffusion’, or TTS).

## Slide 12
average voltage signals created by single electrons entering the MM
not very far from experimental data!
Microbulk (~standard conditions)
Bulk (~standard conditions)

## Slide 13
typical signals in the bulk detector (random selection)

## Slide 14
average over 1000 primary photo-electrons (Edrift=10kV/cm)
Microbulk
Bulk
COMSOL
(simple but nice consistency check!)

## Slide 15
analysis example: typical fitting routine
some small 1-2% 3-sigma tails always present

## Slide 16
fixed threshold
constant fraction
response for typical conditions (bulk) (some technicalities related to analysis)
CFD introduces some correlation with amplitude
(from this point on, only shown the best time resolution attainable)
single-photoelectron
spread from diffusion == == ‘TTS’

## Slide 17
influence of the detector capacitance (CMM)
typical bulk value
Note: signal integrity does not affect timing strongly, but S/N goes down by about 1/10!!
typical microbulk value (35pF)
single-photoelectron

## Slide 18
influence of the mesh transmission (T)
GD*=10, T=1
GD*=10, T=1/8
single-photoelectron

## Slide 19
influence of the pre-amplification (GD)
T=0.07
GD
GD
GD
GD
GD
4
2
(drift field kept constant!)

## Slide 20
influence of the detector technology (microbulk vs bulk)
single-photoelectron

## Slide 21
comparison with data (at fixed drift field)
bulk

## Slide 22
comparison with data (vs field)
bulk

## Slide 23
micro-bulk
= 40
comparison with data (vs field)

## Slide 24
a simple analytical model (R. Veenhof/S. White)
photocathode
no pre-amplification
pre-amplification

## Slide 25
fast look at new laser data
R. Veenhof

## Slide 26
conclusions
MC model allows computing the time response of timing Micromegas. It reproduces the correct time resolution scale, the approximate scaling with number of photoelectrons (~1/√Npe), and the soft dependence with pre-amplification (~ √(log(gain)). Excellent reference for future 3D simulations!!.
The time resolution is nearly independent from capacitance (although signal shapes are strongly affected, sensitivity to single-photon might be lost). Time resolution starts to suffer for BW~100MHz.
Microbulk Micromegas shows worse performance than Bulk, due to lower transmission.
In the single photo-electron case, the CFD-technique introduces some small correlation with amplitude, that disappears for CFD<=0.3.
Operationally, the time response can be approximated through:
σt = TTS/√[Npe x log(gain)]

## Slide 27
next steps
Detailed comparison with new data (~few weeks scale):
  Evaluate different analysis methods (the software stores the complete waveforms!).
  Evaluate in detail the different scalings seen in data…
  Include mips.
What a full simulation (Garfield++) can bring in addition to this?
  Include the exact 3D field (expected to be a small effect, since the field close to the cathode dominates the detector behaviour).
  Include the initial electron energy (this is potentially important, since it drives the extraction efficiency –previous measurements suggest a small effect at present –rather high- operating fields, but things might be different in deep VUV).
  Exact description of the ions and signal waveforms (probably not critical, but nice).
  An exact description of the avalanche statistics is the most important ingredient missing (previous Garfield++ simulations indicate a narrow response for Ne-mixtures --good for single-photon detection. Pure quencher will show larger spreads.)

## Slide 28
Ne/CO2
Ar/CO2
pure exponential (Furry)
Polya
GD=100@200um

## Slide 29
outlook

## Slide 30
Optimum gas mixtures in timing Micromegas?
Look for the minimum time spread (‘fastest mixture’) at any given gain
Simulations from Rob Veenhof
(C2H2F4 from data)
Notes:
Working fields in the MM for pure quenchers need to be about x2 higher. May limit the gain in case of defects.
Drift fields for pure quenchers need to be about x3 higher.
Dissociative attachment for CO2 and freons expected to be compensated by gain. Additional fluctuations will appear. It needs to be verified.

## Slide 31
single-photoelectron
C2H2F4, CF4 anticipate a similar behaviour, but HV stability and photon-feedback need to be overcome!

## Slide 32
appendix

## Slide 33
photo-electron distributions
Note: simulation assumes Furry statistics (Legler model), that is certainly not true for the
Micromegas amplification, but should be a reasonable assumption in the drift.
obtaining single-photon response with UV-lamp will be useful!