## Slide 1: Carrier Board Design
Eduardo Sevilla
3-11-2017

## Slide 2: From Previous Design
3 Updates from previous versions
Clearance for 1800V was wrong in previous Boards. >5mm

## Slide 3: Previous Design

## Slide 4: Update 1
Update of HV+ Clearance (6mm)
Sensor Board (v3)
  Include two TH (SMD is not possible for the Clearance ) Quenching Resistor
  Multiple Bounding for APD signal (Reduce resistor)
  Longer vias for connect with MotherBoard (Vertical Clearance)
  Update the Board Size (32.8x34.6mm2)
Electrical Board (v2)
  Update the Size (32.8x34.6mm2)
  Remove Copper of Bottom Layer
Mother Board (v6)
  Update Carrier Board Vias distribution
  Include internal Regulator (5Vdc 2.5Vdc). Remove 2.5V connector
  Include RC LP filter (5Hz)
  Update pins sockets
  Holes for Screws or fixings
  Update the Board Size (52.6x44.3mm2)

## Slide 5: Update 1

## Slide 6: Update 2
Sensor Board (v4)
  Delete Quenching Resistor (to MotherBoard)
  Update the Board Size (28.2x28.2mm2)
  Include GND vías to drive the Reference Signal
  Update the Pins Layout
Electrical Board (v3)
  Update Board Size (28.2x28.2mm2)
Mother Board (v7)
  Include 1 Quenching Resistor (2 Bigger Board Size)
  Modify HV Connector  2 Connectors (HV+ / Ref) with 2 pins each one (possible 1 per connector)
  Update Transsitors Bias and Output Connector (with threath)
  Update the Sockets for the Carrier Board
  Update the Size (53.2x44.3mm2)

## Slide 7: Update 2

## Slide 8: Update 3
Mother Board (v8)
  Remove the Quenching Resistor
  Remove Fixing Holes
  Reduce the Board Size (47.3x32.8mm2)

## Slide 9: Update 3

## Slide 10: System

## Slide 11: Filling Intermediate Space
Select the Epoxy for filling the “sandwich”
  Intermediate Board instead of Epoxy to separate SensorBoard and ElectricalBoard. Design Intermediate Board
  Epoxy to protect the bounding and the area below sensor top layer.
    Select and buy the epoxy
Select the Process to apply to the Epoxy
  Put it, vacuum and oven

## Slide 12: Filling Intermediate Space

## Slide 13: Filling Intermediate Space

## Slide 14: Filling Intermediate Space

## Slide 15: To Do
Redesign Carrier Board for use with “Negative” Polarity
  Adaptation of AC Coupling Scheme
Manufacture the Boards
Buy Discrete Components
Laboratory Tests

## Slide 16: Schematics

## Slide 17: Schematics