Muon Cooling for a Neutrino Factory and Muon Collider
Muon Front End for a Neutrino Factory and Muon Collider
Chris Rogers,
ASTeC,
Rutherford Appleton Laboratory
15th January 2012

---
High Energy Muon Facilities
High Energy Muon Facilities
- Growing interest in large, high energy muon facilities
  - Neutrino Factory -> neutrino oscillations and
  - Muon Collider -> energy frontier or Higgs factory
- Sizeable R&D effort
  - Muon Accelerator Programme in US
    - Muon accelerator task force called by Fermilab director
  - International Design Study for a Neutrino Factory
- Supported by hardware prototyping
  - Muon Ionisation Cooling Experiment (MICE)
  - Electron Model with Many Applications (EMMA) prototype FFAG
  - Mercury Intense Target (MERIT)
- Such facilities have been made feasible by
  - Fast accelerating, high acceptance accelerators
  - Muon capture conceptual development

---
Neutrino Factory Design
Neutrino Factory Design

---
Neutrino Oscillations
Neutrino Oscillations
- Neutrinos created as superposition of 3 mass states
  - Different phase advance of mass states leads to oscillations between flavour states
  - Lepton flavour violation
  - Matter-antimatter asymmetry (CP violation)
- Governed by fundamental parameters
  - Square mass difference of mass states
  - 3 mixing angles
  - CP violating phase
- Seek to answer fundamental questions of the universe
  - Matter-antimatter asymmetry
- Seek to measure neutrinos precisely to answer these fundamental questions

---
Neutrino Factory Concept
Neutrino Factory Concept
- Seek to manufacture neutrino beam from muon decay
  - Intense, high energy, pure
- Fire neutrinos several thousand km through the earth
  - Measure the change in the admixture of neutrinos
- Gives very sensitive device for analysis of neutrino oscillations
  - Better sensitivties than e.g. LBNE or Beta Beam
  - Beta beam + superbeam is competitive

---
Neutrino Factory Design
- Several iterations
  - 2(4) feasibility studies
  - FS1, FS2, FS2a, FS2b
  - International Scoping Study (2006)
  - International Design Study (IDS) ongoing

---
Proton Driver
Proton Driver
- Neutrino Factory requires a 4 MW proton source
  - 1 MW of SOTA proton sources
  - Demanding but feasible
- Aim for ~ 5-15 GeV proton energy
  - Gives highest pion yield/beam power
  - Gives highest pion yield/shock on target
- Question: what is the challenge with 4 MW proton source?

---
Target
Target
- Intense beam may quickly destroy solid target
  - Proposal to use liquid mercury jet
    - Pipe destroyed by cavitation
    - Jet will be contained by intense solenoid field
  - A PoP experiment recently finished successfully at CERN
    - MERcury Intense Target (MERIT)
- Solid target alternatives under study
20 T pulsed solenoid
Hg Capture
p
Hg Nozzle (injection)
Hg syringe

---
Phase-Energy Rotation
Muon front end
- Beam is very large after pion decay => difficult to control
- Capture longitudinally using fancy RF
- Capture transversely using ionisation cooling
- More in a few slides

---
Recent news: Mice win Nobel Prize

---
Acceleration
Acceleration
- Two technologies in acceleration chain
  - Recirculating Linear Accelerator (RLAs) in dogbone geometry
  - Fixed Field Alternating Gradient machines (FFAGs)
- Enables
  - Acceleration on time scale of muon lifetime
  - Acceleration with large apertures
- Acceleration to 10 GeV

---
Storage Ring
Storage Ring
- Goal: maximize muon decays in straight sections
  - Racetrack, Triangle/Bowtie geometries have been examined
- Racetrack is currently favoured (most flexibility)
  - use long straight sections ~400 m
  - vertical depth of ring can be issue for long baselines
- Use + and -
  - Gives access to measurement of unitarity in neutrino mixing matrix

---
Muon Collider Design
Muon Collider Design

---
Muon Collider Concept
Muon Collider Concept
- Aim is to reach energy frontier lepton collisions using muons
  - Challenge to get sufficiently high luminosity for interesting physics
    - Need lots of cooling
- “High emittance case”
  - Target -> Buncher -> Straight Cooler -> Guggenheim Cooler -> Debunch -> Guggenheim Cooler -> Acceleration
  - Possible to construct a Higgs Factory
  - Possible to construct a 4 TeV lepton collider (or more)
- Can be constructed in stages
  - Neutrino Factory -> Higgs Factory -> 4 TeV Muon Collider
- Cooling technology is the challenge

---
High Emittance Muon Collider
Muon Collider Concept

---
Muon Collider emittance map

---
Roadmap for HEMC (@ Fermilab)
Footprint is on present Fermilab site
HIGGS
FACTORY

---
Muon Front End

---
Baseline Front End
- Adiabatic B-field taper from Hg target to longitudinal drift
  - Drift in ~1.5 T, ~100 m solenoid
- Adiabatically bring on RF voltage to bunch beam
- Phase rotation using variable frequencies
  - High energy front sees -ve E-field
  - Low energy tail sees +ve E-field
  - End up with smaller energy spread
- Ionisation Cooling
  - Try to reduce transverse beam size
  - Prototyped by MICE
  - Results in a beam suitable for acceleration
Taper
Bunch
Rotate
Drift
Cool

---
Secondary Particle Contamination
Significant problem with secondary particles in the front end
  - Potentially activate the entire front end
  - Potentially activate later acceleration system
    - Kickers, septa, etc
  - Additional heat load on e.g. superconductors
  - Not acceptable
Plan is to manage using chicane and proton absorber
  - Chicane removes high momentum particles (p > 500 MeV/c)
  - Absorber removes low energy particles (p < 500 MeV/c)
  - Leaves low energy electrons and muons

---
Particle selection scheme
Bent solenoid chicane induces vertical dispersion in beam
  - Single chicane will contain both signs
    - Opposite signs have dispersion in opposite sense
    - Dispersion is vertical
  - Little disruption to the actual beam
  - High momentum particles scrape
- Subsequent proton absorber to remove low momentum protons
  - Non-relativistic protons don't have much energy, even for relatively large momenta
- Not yet in “baseline” but aim to get it in in next few weeks
p-, m-
p+, m+
proton
absorber
bend
back
p, p-, m-
p+, m+
bend
out
field
taper
target
station

---
Phase-Energy Rotation
- Beam is very large after pion decay => difficult to control
- Seek to manipulate beam in longitudinal phase space
  - Turn energy spread into a time spread
  - Introduce microbunches to enable higher RF frequencies
    - Higher RF gradients
- Allow beam to drift to develop energy time correlation
- Apply RF phased so that front of beam gains more energy than back

---
Muon Ionisation Cooling
z [m]
z [m]
- We have controlled the beam longitudinally – what about transverse?
  - Only technique competitive with muon lifetime is “ionisation cooling”
  - Never before been demonstrated
    - MICE -> Proof of Principle ionisation cooling experiment
  - How does it work?
N(good muons)
Transverse emittance

---
4D Ionisation Cooling
4D Ionisation Cooling
RF
Absorber
- 4D (transverse) cooling achieved by ionisation energy loss
  - Absorber removes momentum in all directions
  - RF cavity replaces momentum only in longitudinal direction
  - End up with beam that is more straight
- Stochastic effects ruin cooling
  - Multiple Coulomb Scattering increases transverse emittance
  - Energy straggling increases longitudinal emittance

---
Time-energy distributions

---
Time-energy distributions
- Now watch the movie
  - Design including chicane/proton absorber
- Look out for
  - Z=30 m – 40 m we have collimation of particles with p >~ 600 MeV/c in the chicane
  - Z = 40 m we have a drop in momentum from the proton absorber
  - Z = 70 m we start to adiabatically form micro bunches
    - At ct=1.5 m intervals until
  - Z = 103 m we start to phase rotate – dephase the cavities so that the tail sees a +ve voltage and the head sees a -ve voltage
  - Z = 141 m we enter the cooling channel... quite a lot of longitudinal loss here, mostly particles that would have been lost later on anyway
  - In fact we probably end the cooling channel at Z=216 m
    - Usually simulate past the maximum
- Note low energy, large ct is the tail of the bunch
  - small ct, high energy is the head of the bunch
  - i.e. small time => arrives at the z plane earlier

---
Ionisation Cooling Menagerie
Ionisation Cooling Menagerie – Straight Coolers

---
Cooling Motivation
Cooling Motivation
- Cooling is important to the Neutrino Factory
  - Increases number of muons by factor ~2
  - Mitigates challenges in high acceptance accelerator and storage ring design
  - More cooling desirable, but cost optimisation issue
- Cooling is vital to the Muon Collider
  - Need to reduce 6D emittance by several orders of magnitude to get to interesting luminosities
- The aim is to increase phase space density of muon beam
  - Requires non-symplectic transport
    - I.e. cannot be achieved with electromagnetic beam elements
  - Instead use some material to “absorb” density
    - “Heats” material
    - “Cools” muon beam
- A number of cooling channel geometries have been proposed with different merits and problems

---
FS2 Channel
FS2 Channel
- Highly optimised cooling channel
  - Liquid Hydrogen absorbers
  - 200 MHz RF
  - SFoFo superconducting coils
  - Best performing linear cooling channel
- Challenging engineering
  - Not cost optimised
  - Detailed engineering design
Total Number of m
Number of m that fit in accelerator

---
FS2A Channel
FS2A/IDS Channel
RF Cell (G4BL)
860 mm
500 mm
5 mm
9 mm
600 mm
0.025 mm
Kill
Lithium Hydride
0.10 mm
Beryllium
- Cost optimisation points to less aggressive cooling
  - Singlet solenoid lattice
  - Solid Lithium Hydride absorbers coated with Beryllium
    - Electromagnetically seal RF cavities to improve Q-Factor

---
B-Induced Breakdown in RF
B-Induced Breakdown in RF
805 MHz RF
Fermilab MTA
Current
configuration
Proposed
- In most designs, solenoid field overlaps cavities
  - Solenoids have extended fringe fields
  - But this magnetic field induces breakdown in the RF cavities
  - Reduces peak achievable gradient by factor ~2
- Investigations under way in the Fermilab Muon Test Area
  - 805 MHz RF tested inside (blue) Lab G magnet
  - Button tests to examine different materials

---
Shielded RF
- Increase cell length to remove RF from solenoid fringe fields
  - Add shielding using iron or bucking coils?
  - Try to keep good acceptance and focusing
- Look at cooling section
  - This is where the RF is most limited
  - This is where optics are most demanding
- How well can we cool in this shielded scenario?
- How well can we optimise the cooling lattice?
- Try to keep RF cavities in < 0.5 T fields
Shielding
RF
Coil
lH2
+
+
-
-
...
...
m

---
Transfer Matrix for a Solenoid
- What is a linear resonance?
- What is criterion for linear resonance in quadrupole channel?
- What is criterion for linear resonance in solenoid channel?

---
Lattice quality
- Two criteria for lattice quality
- b function => how tightly focussed the beam is at the absorber
  - Determines how much cooling we get
  - Require good b function over a large momentum range
- Acceptance => the beam emittance that makes it through the lattice
  - Determines how much beam we get through
- Scale as ~ <Bz2>/p

---
b vs Cell Length
- We want tight focussing on the absorbers for good cooling performance
  - Tight focussing => more cooling
  - Aim for b <~ 1500 mm over ~150 - 300 MeV/c (liquid Hydrogen)
- As cell length gets longer db/dp gets worse
  - Making it hard to contain a beam with a large momentum spread
- Keep cell as short as possible
  - To keep Bz off RF, need to reduce solenoid fringe field

---
Lattice Schematic

---
Capture Performance
IDR performance
- Transmission inside usual cuts:
  - 30 mm normalised transverse acceptance
  - 150 mm normalised longitudinal acceptance
- Note however momentum cut is
  - 173 < Pz < 373 MeV/c for low field geometry
  - 100 < Pz < 300 MeV/c for baseline

---
Straight Magnetic Lattice
SFoFo Magnetic Lattice
coil
Peak field 16 MV/m
Phase 26o
75 cm
coil
coil
50
cm
RF
RF
LH2
LH2
coil
coil
35 cm
43 cm
coil
- Optimise magnetic lattice for (in order of priority)
  - Flat  vs momentum to reduce chromatic aberrations
  - Small  at absorbers to improve cooling
  - Small radius beam to reduce scraping (=>small )
- Choose to use a 10 m long half-cell
  - FS2 was 2.75 m; FS2A was 0.75 m
- Alternating B-field to conserve canonical angular momentum
  - Make field 0 at absorber so that kinetic angular momentum is 0
  - Then kinetic angular momentum does not change in absorber
  - So canonical angular momentum conserved
size 12{ sqrt {β} } {}

---
Field and beta function
Field and beta function
 [mm]
Bz [T]
z [mm]
z [mm]
- Convenient shoulders in function for RF cavities
  - These are still the limiting aperture
  - Scraping here limits performance
- Tight focus at the absorbers improves cooling
  - Lessens the effect of heating due to Multiple Coulomb Scattering
- Large  in centre forces central coil to high radius
  - Becomes more expensive

---
Momentum Dependence
Momentum Dependence
 [mm]
500
400
E [MeV]
E [MeV]
E [MeV]
E [MeV]
- 2nd order, transverse aberrations dependent only on energy spread
  - Try to remove non-linearities by making  function constant with p
  - Restricts transverse energy spread
- 2nd order longitudinal aberrations dependent on phase advance
  - Leads to correlation between momentum and transverse amplitude
- Resonances when cos()>1
  - Lattice is not focussing at these momenta
cos()

---
Linear Cooling Performance
Capture Performance
A = 100 mm
Figure of Merit
1.24
1.40
1.50
1.56
Length [m]
80
160
240
400
A = 15 mm
- Use same figure of merit
  - Number of  in some accelerator acceptance
  - Cooling performance for long, straight cooling channel only
- Comparable cooling performance to FS2A but still not as good
  - More expensive
  - But RF cavities no longer sit in such strong B-fields
Figure of Merit

---
Movie

---
Ionisation Cooling Menagerie – Recirculating Coolers

---
Recirculation - Benefits
- Recirculating beam => reuse hardware
  - Makes cooling device cheaper
- Recirculating beam => improved cooling
  - Special technique “emittance exchange”
- However
  - Difficult to get the device to work...

---
Dispersive beams
Dispersive beams
- Introduce bends into beamline
  - Now off-momentum particles follow a different trajectory to on-momentum particles
- Consider cell-by-cell closed orbit
  - Dispersion is the distance between the on-momentum closed orbit and an off-momentum closed orbit
    - Normalised to the momentum difference
- Dispersion is a 1st order effect
- In solenoid-dipole channels dispersion is 2D
  - Rotation between x and y turns an offset in x into an offset in y
D
p0+dp
p0

---
Emittance Exchange
Emittance Exchange
Wedge
RF
- Ionisation cooling cools in transverse phase space
  - But longitudinal emittance is also large
  - It would be useful to cool in longitudinal and transverse phase space
- Emittance exchange takes emittance from longitudinal phase space to transverse
  - Introduce dispersion => higher energy muons have larger radius
  - Wedge absorber takes more energy from large radius muons
- This is a shear in x-E phase space
  - Does not cool the beam (to 1st order)
- But together with transverse cooling provides 6D cooling
Dipole

---
Ring Cooler
Ring Cooler
- RFoFo cooler makes bending field using tilted coils
  - Ring circumference 33 m
- Improves number of muons into small acceptance by ~100s
- But a number of challenges
  - Injection is highly challenging
  - Heat load on absorbers is demanding
  - RF breaks down in high Bz

---
Guggenheim Cooler
Guggenheim Cooler
- Pull ring out into a helix
  - Solve absorber heating
  - Solve kicker issue
- Need B-shielding between floors
- Leaves RF sitting in high Bz
- Performance comparable to ring
  - But need to buy much more hardware $$
  - Need one for each sign

---
Helical Cooler
- Change aspect ratio of the Guggenheim
  - May make Guggenheim more compact
  - RF cavities built into the magnet

---
“High Emittance” Muon Collider

---
Muon Ionisation Cooling Experiment
Muon Ionisation Cooling Experiment

---
MICE 4D Cooling PoP
MICE 4D Cooling PoP
- Proof of principle muon ionisation cooling cell
  - Under construction at Rutherford Appleton Laboratory
  - Beamline, AFC, RF, trackers, PID detectors
- Aim to understand engineering risks and prove physics modelling

---
Beam Dynamics
Beam Dynamics
- MICE designed to run at a number of different settings
  - Different momenta
  - Field flipping and non-flipping
  - Different focussing at absorbers
  - Different absorber materials
  - Different input beams
- Baseline case is 200 MeV
  -  tightly focussed at absorbers
  - Bz 0 in absorber material
    - For angular momentum conservation
  - Additional focussing in RF cavities
    - To prevent excessive scraping

---
Momentum Acceptance
Momentum Acceptance
- Lattice design for high momentum acceptance
  - Means staying clear of linear resonances
- Understand resonances ito Fourier components of on-axis B-field
  - Each resonance controlled by a Fourier Component
- MICE is an “SFoFo-type” lattice
  - Suppress fourier components that would give linear resonances
- MICE has wide acceptance band in range 150 < Pz < 250 MeV/c
  - Weak stop band at ~195 MeV/c

---
Cooling Performance
Cooling Performance
- MICE gives ~ 10% emittance change
  - Optical heating
  - Absorber cooling
- Cooling gives an increase in muon density at MICE centre
- Heating gives an increase in muon density at MICE fringe
- Hope that cooling is faster than heating!

---
Measurement Performance
- In emittance measurement Detector error is a systematic effect
  - MICE measures beam width etc
  - Errors in position measurement add to beam width measurement in quadrature
  - Given a good knowledge of detectors this error can be removed
  - Gives high precision emittance measurement
- Aim is to measure emittance change to ~ 1%
  - Challenging
  - But simulations indicate it can be done!

---
Conclusions
Conclusions
- Growing interest in large, high energy muon facilities
  - Neutrino Factory -> neutrino oscillations
  - Muon Collider -> energy frontier or Higgs factory
- Such facilities have been made possible by
  - Fast & high acceptance accelerators
  - Revolution in muon cooling conceptual design
- Muon cooling is a challenging technology
  - High acceptance accelerators
  - High gradient RF
  - Superconducting solenoids
- Soon to be proved by experiment
  - MICE construction underway