Muon Cooling for a Neutrino Factory and Muon Collider
Reoptimising Front End with proton absorber
Chris Rogers,
ASTeC,
Rutherford Appleton Laboratory

---
High Energy Muon Facilities
Proton absorber integration
- Adding a proton absorber skews the energy-time distribution of the outgoing muon beam
- Hope that adding a drift space would let it re-align
- That doesn't work
- Need to re-optimise the buncher and phase rotation to cope
- Prefer to work in g4beamline
  - Chicane is in g4beamline
- Need to develop optimisation routine
  - Make optimisation wrapper around g4bl
  - First check for straight lattice

---
Optimisation Routine
- 1D Model
  - RF Cavity model
    - Energy gain is sine wave
    - Standard transit time factor calculation
  - Implement energy loss routine to get nominal energy loss in Beryllium
    - Linear interpolation off PDG energy loss table
- Track high momentum and low momentum particle through
- Use time difference to set RF frequencies
  - As in icool routines
- Here, try linear ramp in voltage followed by linear ramp in phase on the second reference particle
  - i.e. the usual buncher followed by the usual phase rotation

---
No absorber – ICOOL simulation
45 bunch cavities
60 rotator cavities
14 bunches (140-233 MeV/c)
Rotator phase 16 degrees
Rotator voltage 13 MV/m

---
No absorber
time_energy_movie-0mm.avi

---
Optimisation Routine
- Performance in ICOOL
  - Longitudinal emittance is well controlled
  - Still some longitudinal mismatch on entry to the cooling channel
  - Good muon rate is encouraging
- Note
  - No windows
  - Increased LiH absorber thickness in cooling channel (12 mm)

---
100 mm absorber – ICOOL simulation
50 bunch cavities
65 rotator cavities
14 bunches (140-233 MeV/c)
Rotator phase 15 degrees
Rotator voltage 13 MV/m

---
No absorber
time_energy_movie-100mm.avi

---
Optimisation Routine
- Performance in ICOOL
  - Longitudinal emittance is not so well controlled
  - Cavities dephase to ~ 1 ns == 100 deg phase
  - Cooling channel not simulated

---
So...
- Optimisation using a simple 1D model works when no proton absorber
- Introducing a proton absorber screws up the 1D model
  - Energy loss from G4 is slightly different – enough to misphase cavities