Muon Cooling for a Neutrino Factory and Muon Collider
7 Cell RF and Low B-Field Channel
Chris Rogers,
ASTeC,
Rutherford Appleton Laboratory

---
Two items
Duplicated Diktys's result of number of cells in RF
Low B-field cooling channel implemented in ICOOL

---
Number of Cells in RF
Discussed 4 weeks ago increasing number of RF cells in cooling channel per gap
Diktys simulations indicate marginal increase in muon yield for 7 RF cells per bellows as opposed to 5 RF cells per bellows
Neil Collomb (DL Engineering) ambivalent as to whether we have 7 RF cells or 5 RF cells
As long as it fits on a crane...
We have to worry about alignment tolerances
Rogers simulations (below, g4bl only) confirm Diktys result
Propose to modify the baseline to include 7 RF cavities

---
G4BL

---
Low B-Field Cooling Channel
ICOOL
Diktys requested ICOOL version of the Low B-Field cooling channel FE lattice
Overall field looks good
Overall rate looks similar
Main difference is better aperture control in ICOOL
Leads to lower transverse emittance (scraping)
Leads to lower total rate
About the same rate in n_1
Less noise/better matching
Nb: g4bl uses slightly realistic coils; icool uses ideal 1.5 T field

---
LiH Lattice Schematic
LiH length	46 mm
RF peak field	19 MV/m
RF phase	30 degrees
RF length	500 mm
Be window thickness	0.4 mm
Apertures	400 mm
Coil length	1000 mm
Coil radial thickness	100 mm
Coil inner radius	400 mm
Coil current	19 A/mm2

---
Bz

---
Bz and beta

---
Transmission and eps_perp

---
Good muon rate
0.0788
m+/p