Muon Cooling for a Neutrino Factory and Muon Collider
Integrating Chicane in G4BeamLine
Chris Rogers,
ASTeC,
Rutherford Appleton Laboratory

---
High Energy Muon Facilities
More on G4Beamline Lattice
- Effect of coil geometry on G4Beamline lattice
- Placement of proton absorber – straight lattice
- Placement of proton absorber – chicane
- Optimisation
- Proton power deposition with chicane/absorber system

---
Effect of coil geometry on G4BL
- Now have a full coil geometry implemented in G4BL
  - Removed constant 1.5 T field
  - Replaced with two sections of coils inspired by FS2A lattice
    - Small coil 430 mm inner radius for Drift
    - Large coil 650 mm inner radius for Buncher/Rotator (to accomodate RF)
  - Three bits of “matching”
    1. Matching from capture solenoid into 1.5 T region
    2. Matching from small coils to large coils
    3. Matching from large coils to cooling lattice
  - Necessary precursor to implementing chicane

---
Matching - Capture -> 1.5 T
2 %

---
Matching – 1.5 T -> Cooling

---
Performance

---
Performance

---
Optimisation of combined proton absorber, chicane system
- When proton absorber and chicane included, optimise over 4 parameters
  - Proton absorber thickness
  - Drift length
  - Absorber position
  - Chicane angle
- Start with just proton absorber
- Then just chicane
- Then full system
- (Optimisation not finished)

---
Muon rate
Add proton absorber
Try to fix longitudinal phase space
Optimise on position of absorber
Optimise on length of drift
Mu+/proton
Mu+/proton
Mu+/proton
Mu+/proton
Mu+/proton

---
Proton absorber, No Chicane
Compare with power remaining in proton beam

---
Proton absorber, No Chicane
Proton absorber thickness [mm]	Maximum rate (mu+/proton)	Proton beam power [%]
0	0.1171	100
50	0.103	90.9
100	0.08714	82.4
200	0.08374	70.9
300	0.06805	60.6
Ultimate figure(s) of merit is mu+/proton compared to proton beam power leaking into downstream accelerator

---
Chicane, no proton absorber
Mu+/proton

---
Chicane, no proton absorber
Chicane / dθ [o]	Maximum rate (mu+/proton)	Proton beam power [%]
0	0.1171	?
1.0	0.1091	?
1.25	0.1047	?
1.5	0.0975	?
1.75	0.1006	?

---
100 mm proton absorber + chicane
Absorber in
buncher
Mu+/proton
Mu+/proton
Mu+/proton

---
200 mm proton absorber + chicane
Mu+/proton
Mu+/proton
Mu+/proton

---
Chicane, no proton absorber
Clean up of input deck
Optimisation ongoing
Final step:
Plot dθ vs absorber thickness vs muon rate
Plot dθ vs absorber thickness vs proton power
Choose parameters, rebaseline
Looks like we will get a hit on muon rate