   SHIELDING STUDIES FOR IDS80 (NO IRON PLUG/YOKE),
        ADDING SHIELDING IN 75 TO 80 cm (WC/H2O, B, Cd) .
NICHOLAS SOUCHLAS (BNL)
Dec. 14, 2010‏
        ‏
1

---
Energy deposition from MARS+MCNP codes
(10-11 MeV NEUTRON ENERGY CUTOFF).
IDS80 GEOMETRY WITHOUT IRON PLUG AND YOKE MATERIAL (TO ACCOMODATE ACCESS TO DIFFERENT PARTS OF THE TARGET STATION).
SHIELDING (60%WC+40% H2O)+ SHIELDING FROM 75 TO 80 cm (60%WC+40% H2O or 20%B10+80%B11 or Cd)
4MW proton beam. Np=400,000
PROTONS ENERGY E=8 GeV.
GAUSSIAN PROFILE: σx=σy=0.12 cm.
2

---
IDS80 GEOMETRY WITH AND WITHOUT IRON PLUG AND YOKE.
NEW: SC#1-7 -300<z<345 cm Rin=80.0 cm Rout=140 (1)/160 (2,3)/115 (5-6)/108(7) cm(NbSn)
        SC#8-10 383<z<667 cm Rin=72/63/54 cm Rout=97.0/83/69 cm (NbTi)‏
        SC#11-14 700<z<1090 cm Rin=45 cm Rout=51 cm (NbTi)
        SC#15-21 7190<z<1090 cm Rin=45 cm Rout=49 cm (NbTi) (TOTAL # SC=21)‏
  3

---
INSERT ADDITIONAL SHIELDING (WC, B/H2O, CD) BETWEEN 75 AND 80 cm RADIUS, AROUND INTERACTION AREA.
  4

---
ENERGY DEPOSITED IN SC SOLENOIDS (SC#), SHIELDING (SH#).
 5

---
ENERGY DEPOSITED IN RESISITVE SOLENOIDS (RS#),
   BEAM PIPE(BP#).
 6

---
ENERGY DEPOSITED IN DIFFERENT PARTS OF TERGET STATION: OTHER PARTS, TOTALS, PEAK VALUES.
7

---
PEAK VALUES OF DEPOSITED ENERGY IS SC#1-7, SC#11-14
75<r<cm VACUUM (105 events).
PEAK VALUES IN mW/gr(SC#11-14)
PEAK VALUES IN mW/gr(SC#1-7)
8

---
PEAK VALUES OF DEPOSITED ENERGY IS SC#1-7, SC#11-14
75<r<cm VACUUM (4.105 events).
PEAK VALUES IN mW/gr(SC#1-7)
PEAK VALUES IN mW/gr(SC#11-14)
9

---
PEAK VALUES OF DEPOSITED ENERGY IS SC#1-7, SC#11-14
75<r<80 cm 60%WC+40%H2O(4.105 events).
PEAK VALUES IN mW/gr(SC#1-7)
PEAK VALUES IN mW/gr(SC#11-14)
10

---
PEAK VALUES OF DEPOSITED ENERGY IS SC#1-7, SC#11-14
75<r<80 cm 80%B10+20%B11(4.105 events).
PEAK VALUES IN mW/gr(SC#1-7)
PEAK VALUES IN mW/gr(SC#11-14)
11

---
PEAK VALUES OF DEPOSITED ENERGY IS SC#1-7, SC#11-14
75<r<80 cm CADMIUM (CD)(4.105 events).
PEAK VALUES IN mW/gr(SC#1-7)
PEAK VALUES IN mW/gr(SC#11-14)
12

---
ADDITIONAL SLIDES

---
STUDY II GEOMETRY 3D ROOT PLOT OF DEPOSITED ENERGY FOR FIRST TWO SUPER-CONDUCTING SOLENOID:5.5 mW/gr ~(64.5<r<67.0 cm, -20.0<z<32.0 cm)
  21

---
STUDY II
IDS80 IRON PLUG
IDS80 NO IRON PLUG
STUDY II PEAK VALUE: ~(5.5 mW/gr in -20.0<z<32.0 cm, 64.5<z<67 cm) SC#1
IDS80 PEAK VALUE: ~(0.36 mW/gr in -42.0<z<9 cm, 80<r<81.2 cm, 82.2<r<84.5 cm) SC#4
IDS80 NO IRON PLUG PEAK VALUE: ~(0.36 mW/gr -19.0<z<44.0 cm, 80.5<r<81.0 cm) SC#3
  22